## Slide 1
VIABILIDAD TECNICO ECONOMICA
para un suministro eléctrico 100% renovable en España
Dr. Santiago Galbete Goyena
Mayo 2017

## Slide 2
EVOLUCION SISTEMA ELECTRICO ESPAÑO 2001-2016
1
Chart: EVOLUCION DEMANDA ELECTRICA ESPAÑA 2001-2016
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Demanda Eléctrica | 1 | 1.0286 | 1.0983 | 1.1476 | 1.1972 | 1.2401 | 1.2762 | 1.2896 | 1.2264 | 1.2673 | 1.2409 | 1.224 | 1.1971 | 1.1858 | 1.2069 | 1.217
Potencia Demanda Máxima | 1 | 0.98299 | 1.0796 | 1.08 | 1.2419 | 1.2068 | 1.2847 | 1.2299 | 1.2723 | 1.2632 | 1.2627 | 1.2461 | 1.1531 | 1.115 | 1.1659 | 1.1591
Potencia Instalada | 1 | 1.0846 | 1.1284 | 1.246 | 1.3412 | 1.4309 | 1.5652 | 1.6484 | 1.7146 | 1.7958 | 1.8236 | 1.8463 | 1.8545 | 1.8541 | 1.8605 | 1.8148
Chart: POTENCIA RENOVABLE Y CICLO COMBINADO MW
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Renovables sin GH | 5337 | 7055 | 8469 | 10945 | 12497 | 14258 | 18027 | 21960 | 25274 | 27238 | 28683 | 31866 | 32520 | 32661 | 32661 | 32682
Ciclo Combinado | 0 | 3136 | 4347 | 8233 | 12224 | 15504 | 20962 | 21677 | 23066 | 24948 | 24948 | 24948 | 24948 | 24948 | 24948 | 24948
Chart: Horas (año)
Producción potencial renovable vs demanda = 0.24 España 2007
Producción potencial renovable vs demanda = 0.24 España 2007
Chart: Horas (año)
Producción potencial renovable vs demanda = 0.6 España 2007
Producción potencial renovable vs demanda = 0.6 España 2007
Ley 54/1997
RD 436/2004
Ley 661/2007
Ley 1/2012
Ley 1/2013
RD 413/2014
Conclusión:
Necesidad de almacenamientos reversibles
Misma solución que la generación nuclear

## Slide 3
Chart: 
| Large Hydro | Wind | Solar | Mini Hydro | Biomass | Nuclear | Coal | Gas | Other no renewables
Ventas | 17.3 | 22.2 | 6.6 | 2 | 1 | 7.7 | 10.9 | 24.9 | 7.4
41.4%
58.5%
Spain overview
255 TWh
22.8%
6.7%
25%
6.7 %
Wind
Gas
Large Hydro
100.1 GW
Renewable generation
INSTALLED CAPACITY
ELECTRIC GENERATION
2016
18.2%
Solar
Mini Hydro
2%
1%
Biomass
7.7%
Nuclear
9,52%
Coal
CHP
TECNHICAL AND ECONOMIC VIABLILITY of a 100% electric renewable supply in Spain
2
51% Renewable
38.2%
61.8%
Non Renewable generation
2016
2015
  Connection with France: 2.8 GW (1.4 GW 2014)
  100% Electric renewable supply is the only sustainable option (economically and enviromentally)
No gas, no oil, no uranium
Coal quality is very poor : 95% imported
  High potential: Wind, sun, hydro
Electrical isolated country
Resources
Last fuel plant (520 MW) has been decommisioned , 2015
9% of the total coal power plants decomissioned (1,4 GW), 2016
A new 854 MW pump hydro plant has been commisioned, 2016
3 GW Wind technologie have been awarded, may 2017
2015 -2017

## Slide 4
Large hydro
17
62 (6.7 GW)
75 (22.9 GW)
19 (17 GW)
5 (0 GW)
6 (1 GW)
Renewable and storage resource
Total
PV on the land
PV on the roof,
Madrid 4 GW
Wind-Offshore
Wind-Onshore
Binary cycle
EGS
42
20
70
5
Residual Biomass
New energetic crops*
Rotation of existing forest
3
2
1
Mini hydro
2
4
1
Solar
Wind
Geothermal
Hydraulic
Biomass
*occupation of the territory
RESTRICTION 2
Pump Hydro storage
TECNHICAL AND ECONOMIC VIABLILITY of a 100% electric renewable supply in Spain
Potential Renewable Power (GW)
Installed capacity 2016 (GW)
Potential: 7 GW
Installed: 3.5 GW
question mark
167 GW RESTRICTION 1
Batteries
Riverland Australia March 2017:
330 MW PV
100 MW/440 MWh Storage
1.1 Million batteries (20% daily production)

## Slide 5
Condiciones y estrategia para conseguir un suministro 100% renovable en España
Priorizar las fuentes renovables no controlables (sol y viento) , tecnologías maduras
Gestionar las plantas hidráulicas de gran potencia para cubrir las deficiencias del sol y viento
Gestionar los almacenamientos reversibles (bombeo) para maximizar el aprovechamiento de las fuentes renovables no controlables (sol y viento)
Controlar plantas de biomasa como fuentes renovables controlables para cubrir las deficiencias del resto de las plantas
Garantizar el 100% de la demanda eléctrica
El coste del sistema renovable no debe ser superior al del sistema no renovable
Condiciones requeridas
Estrategia para conseguir un suministro eléctrico 100% renovable
TECNHICAL AND ECONOMIC VIABLILITY of a 100% electric renewable supply in Spain

## Slide 6
1.4%
0.4
0.6
0.8
1
1.2
1.4
1.2%
1%
0.8%
0.6%
0.4%
0.2%
0%
Renewable Penetration
Low controllable penetration (scenario 2)
High controllable penetration (scenario 1)
Reversible storage capacity vs Demand (%)
Restrictions 1&2
6%
4%
2%
0%
8%
0.5
1
0
1.5
2
Renewable Penetration
Without large hydro
With large hydro
Se requiere buscar la combinación óptima entre generación renovable y almacenamiento para conseguir un suministro 100% renovable
Curva de almacenamiento crítico y zona apta
Recursos limitados (fuentes renovables y almacenamineto)
TECNHICAL AND ECONOMIC VIABLILITY of a 100% electric renewable supply in Spain
Restrictions 1&2
Reversible storage capacity vs Demand (%)

## Slide 7
100% renewable electric supply scenarios in Spain
TECNHICAL AND ECONOMIC VIABLILITY of a 100% electric renewable supply in Spain
3.5
System 2016
2.1
Total 100.1 GW
0.9
15
6.7
22.9
100% renewables System 2
Total 118.3 GW
2.0
11.8
6.1
17.0
27.0
3.6
50.3
100% renewables System 1
2.0
8.3
9
17.0
33.5
3.6
59
Total 132.4 GW
A 100% electric system in Spain in 2050 is technically feasible
Non renewable
Biomass + Geothermal
Pumped hydro
Hydro
On shore wind
Mini Hydro
Solar
Off shore wind
WHEN?
49.5

## Slide 8
LCOE valor tecnologías a 2050 k=8%, i=3,5%
2050 is a reference year for many sources
ECONOMIC VIABLILITY of a 100% electric renewable supply in Spain
No environmental damages are considered
PV on the land LCOE has decreased considerably
Wind and Sun LCOE are in the same range as nuclear. Bloomberg
7
LCOE Forecast 2050
TECHNOLOGY | LCOE 2011 €/MWh | Investment % | O&M % | Resource % | Environment €/MWh | LCOE 2050 €/MWh
Wind Onshore | 74 | -10 | -20 | NA | NA | 65
Wind Offshore | 114 | 0 | 0 | NA | NA | 114
PV on the floor | 71 | -15 | -30 | NA | NA | 58
PV on the roof | 119 | -60 | -50 | NA | NA | 49
STEG Parabolic Trough | 269 | -50 | -50 | NA | NA | 135
STEG Tower with storage | 260 | -65 | -50 | NA | NA | 103
Municipal Solid Waste | 104 | -50 | 0 | 0 | NA | 64
Biomass (straw, pruning, existing forest) | 117 | -20 | -15 | 0 | NA | 107
Biomass (energetic crops) | 196 | -20 | -15 | -30 | NA | 143
Binary cycle Geothermal | 75 | -50 | -50 | NA | NA | 37
EGS Geothermal | 150 | -30 | -40 | NA | NA | 99
Large Hydro | 64 | 0 | 0 | NA | NA | 64
Pumping Hydro | 98 | 0 | 0 | NA | NA | 98
Mini Hydro | 56 | 0 | 0 | NA | NA | 56
Nuclear | 72 | 20 | 0 | 25 | 15 | 94
Gas | 52 | 0 | 0 | 50 | 10 | 91
Coal | 53 | 100 | 0 | 40 | 0 | 73
Cogeneration | 52 | 0 | 0 | 50 | 10 | 91

## Slide 9
96.3%
2050 |  |  |  | 
i % | K % | Actual €/MWh | 100% Ren. €/MWh | 100% Ren. Vs actual
3.5 | 8 | 85.2 | 82.0 | 96.3%
2011 |  |  |  | 
i % | K % | Actual €/MWh | 100% Ren. €/MWh | 100% Ren. Vs actual
3.5 | 8 | 68.6 | 107.1 | 156.1%
ECONOMIC VIABLILITY of a 100% electric renewable supply in Spain
A 100% electric system in Spain in 2050 is economically feasible, for any disccount and inflation rates
8
Electricity cost: current mix versus 100% Renevable
LCOE 2011 versus 2016
2015 |  |  |  | 
i % | K % | Actual €/MWh | 100% Ren. €/MWh | 100% Ren. Vs actual
3.5 | 8 | 101,5 | 87,1 | 86.7%
Sensibility study: discount and inflation rates

## Slide 10
96.3%
ECONOMIC VIABLILITY of a 100% electric renewable supply in Spain
PV, large plants and very high module price decrease, Nuclear CAPEX important increase
9
Wind On Shore, PV and Nuclear LCOE
LCOE 2011 versus 2016,

## Slide 11
80%
60%
40%
20%
0%
Power vs Peak Power
TECNHICAL AND ECONOMIC VIABLILITY of a 100% electric renewable supply in Spain
Renewable delivered directly to the grid
Renewable contrallable
Large hydro storage
Reversible storage
No renewable controllable
No renewable no controllable
0
50
100
150
200
250
300
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
1.1
1.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
1.1
1.2
RPPR
RPPR
Non renewable power installed during the transition process
TWh
10
Energy supply
Combined Cycle Power: Controllable Nuclear Power: Non Controllable
Transition Process to a 100% electric renewable system

## Slide 12
Un suministro 100% renovable es el único camino para un desarrollo económico a largo plazo
El proceso de transición requiere:
Un sistema eléctrico 100% renovable en España es:
Conclusiones
TECNHICAL AND ECONOMIC VIABLILITY of a 100% electric renewable supply in Spain
Técnicamente viable. Recurso suficiente y la potencia renovable necesaria esta en el mismo rango que la potencia actual: 100 MW actuales versus 132 GW renovables
Económicamente viable, actualmente el sistema 100% renovable sería del orden de un 13% más económico que el sistema actual
Es el único camino para un desarrollo económico a largo plazo
El almacenamiento es un factor crítico para conseguir un suministro eléctrico 100% renovable: Gran hidráulica y reversible (bombeo y baterías)
El sistema actual dispone de la potencia en plantas convencionales controlables necesaria para el proceso de transición. Estas deberán estar activas prácticamente hasta el final del proceso de transición.

## Slide 13
VIABILIDAD TECNICO ECONOMICA
de un suministro eléctrico 100% renovable en España
email: sgalbete@acciona.es